## Slide 1: Adjoint Inverse Designed Metasurfaces with Visible Multiwavelength Steering
INTEGRATED
PHOTONIC
DEVICES&
SYSTEMS LAB
2021. 7. 7
백웅재, 김휘
일리노이 대학교
고려대학교

## Slide 2
INTEGRATED
PHOTONIC
DEVICES&
SYSTEMS LAB
Contents
Introduction (Metagrating)
Adjoint Inverse Design
Topology Optimization Method
Simulation Result
Conclusion (GSS & Robustness)

## Slide 3
Introduction
Metagrating
Effective Medium
Transmit Array
Echelle
Geometric Phase
Neshev, D., Aharonovich, I. Light Sci Appl 7, 58 (2018)
Conventional Way: Implement regularly spaced nanowaveguides or nanoresonators
What is the most effective way for producing a metasurface with a desired phase profile?
10%
30%
40%
75%

## Slide 4
Adjoint Inverse Design
Inverse Design Concept
SiO2
Substrate
Air
Visible Light
Grating
Grating Purpose: Diffraction to target order
State-of-the-art example
Jonathan Fan, Nano Lett. (2017)

## Slide 5
Adjoint Inverse Design
Adjoint Inverse Design Theory
Vector Wave Equation
Optimization Target
Discretization
Lorentz Reciprocity

## Slide 6
Adjoint Inverse Design
Adjoint Inverse Design Theory

## Slide 7
Topology Optimization Method
Meta-Optics Inverse Design Framework
Forward Simulation
Adjoint Simulation
Random permittivity profile (Gaussian Blurred for clustering)
For each iteration,
the forward and adjoint simulations are:
ADAM
+
Iteration m
Iteration m+1
Gaussian Filter

## Slide 8
Topology Optimization Method
Design Flow Chart
Initial Metagrating
Pattern Design
Clustering by
Gaussian Blurring
Determine Optimization Cost Function
(Figure of Merit)
Max
Initial Binarization
Calculate FoM
(Gradient)
Updated Gradient
ADAM
Enforce Symmetry
Update Pattern
Enforce
Symmetry
Enforce
Symmetry
Binarization
Updating Pattern
Meet Criterion?
Final Meta-Design
Simulation Verification
1) Field Visualization
2) Efficiency Calculation
3) Processable Structure Check
Optimization Loop
i=1 m
FMM
Forward
Simulator
FMM
Adjoint
Simulator
No
Yes
Gaussian
Blurring
Optimization Begins

## Slide 9
Simulated Results
Topology Optimization
After 200 epoch

## Slide 10
Simulated Results
Topology Optimization
Simulation parameter
Tx = 780nm
Ty = 330nm
Number of sampling = 101×101
Polarization mode = TM
Substrate = 1um(SiO2)
Grating = 400nm(c-Si)
Red (620nm)
Absolute Transmittance: 85.1%
Target Diffraction Order: +1 st
Diffracted Angle: 52.6 (deg)

## Slide 11
Green (532nm)
Absolute Transmittance: 80.0%
Target Diffraction Order: 0 (DC)
Diffracted Angle: 0 (deg)
Simulated Results
Topology Optimization
Simulation parameter
Tx = 780nm
Ty = 330nm
Number of sampling = 101×101
Polarization mode = TM
Substrate = 1um(SiO2)
Grating = 400nm(c-Si)

## Slide 12
Blue (473nm)
Absolute Transmittance: 76.2%
Target Diffraction Order: -1st
Diffracted Angle: 37.3 (deg)
Simulated Results
Topology Optimization
Simulation parameter
Tx = 780nm
Ty = 330nm
Number of sampling = 101×101
Polarization mode = TM
Substrate = 1um(SiO2)
Grating = 400nm(c-Si)

## Slide 13
Simulated Results
Topology Optimization
Red
Green
Blue
Incident beam
(White)
0th
+1st
-1st
780 nm
330 nm
Deflected beam
0th
+1st
-1st
Beam Splitter
Beam Combiner

## Slide 14
Topology Optimized Result
Simulation parameter
Tx = 1200nm
Ty = 450nm
Number of sampling = 101×101
Polarization mode = TM
Substrate = 1um(SiO2)
Grating = 400nm(c-Si)
Simulated Results

## Slide 15
Additional Optimization Routine
Simulated Results
Step 1. Find an optimized initial pattern using only Red and Blue gradient  Will be optimized in Red and Blue only (no control over Green: )
Step 2. After finding an optimized initial pattern that optimizes Red and Blue efficiently, use the same initial pattern to find RGB optimized pattern via controlling

## Slide 16
Step 1 Result
Simulation parameter
Tx = 1200nm
Ty = 450nm
Number of sampling = 101×101
Polarization mode = TM
Substrate = 1um(SiO2)
Grating = 400nm(c-Si)
Simulated Results

## Slide 17
Step 2 Result
Simulation parameter
Tx = 1200nm
Ty = 450nm
Number of sampling = 101×101
Polarization mode = TM
Substrate = 1um(SiO2)
Grating = 400nm(c-Si)
Simulated Results

## Slide 18
Simulated Structure Field Visualization
Simulated Results
Adjoint
Forward
Red
Green
Blue

## Slide 19
Simulated Structure Field Visualization
Simulated Results
Red
Incident
R/G/B
Red
Green
Blue
Green
Incident
Blue
Incident

## Slide 20
Adjoint Inverse Design Theory
R/G/B Steering Metagratings Design
Multiwavelength Steering Metagrating in one layer
Further reducing computational cost via additional algorithm
Conclusion
Summary
Future Works
Finding processable structure by adopting appropriate binarization and gaussian blurring
Enhanced optimization: Golden Section Search

## Slide 21
Thank you for your attention

## Slide 22
Appendix
Effective Medium
Transmit Array
Echelle
Geometric Phase
Types of metasurface and its efficiency

## Slide 23
Appendix
Scalar Fourier Modal Method
Step 1: Slicing region of interest & Stair-case approximation
Step 2: Eigenmode analysis for each layer
Step 3: Boundary conditions & Scattering Matrix
Step 4: S-matrix method for interconnecting multi-block structures

## Slide 24
INTEGRATED
PHOTONIC
DEVICES&
SYSTEMS LAB
Discretized Variational Form based Adjoint Inverse Design Theory
Discretization
We can discretize the electric and magnetic field into N number of local fields
Discretization
Vector Wave Equation
Let,

## Slide 25
INTEGRATED
PHOTONIC
DEVICES&
SYSTEMS LAB
Discretized Variational Form based Adjoint Inverse Design Theory
Figure of Merit
Variation Method
(using nodal complex Lagrange multiplier)
We want to know the change in FOM as the structure varies:
Solving above equations: (use the first two terms as constraints)

## Slide 26
INTEGRATED
PHOTONIC
DEVICES&
SYSTEMS LAB
Discretized Variational Form based Adjoint Inverse Design Theory
Solving Lagrange Multiplier
Source terms

## Slide 27
INTEGRATED
PHOTONIC
DEVICES&
SYSTEMS LAB
Discretized Variational Form based Adjoint Inverse Design Theory
Calculating Sensitivity

## Slide 28
light input
Optimization Problem

## Slide 29
light input
light input
light input
…
Where should I add material?
Need to know dF/dx’ for all x’

## Slide 30
What happens when I add material?
E0
Original
Perturbation = small sphere of material
ε1
P
ε2
Eperturbed
ε1

## Slide 31
How can I approximate this perturbation?
E0
Escattered
Eperturbed
+
≈

## Slide 32
Key Trick 1: (approximate every perturbation as a dipole scatterer)
…
…
+
+

## Slide 33
Drive a dipole at x’
Find E at x0
Drive a dipole at x0
Find E at x’
equivalent
Reciprocity (Rayleigh-Carson)

## Slide 34
equivalent
J1  E3 = J3  E1
J1(x’)
E1
J2(x’’)
E2
Problem: Solve for E1 and E2
Dual Problem: Solve for E3
J3
E3(x’)
E3(x’’)
J2  E3 = J3  E2
Reciprocity (Lorentz)

## Slide 35
Key Trick 2: (Lorentz reciprocity)
+
…
+